## Slide 1: MOSH NOISE TEAM Activities
12 November 2013

## Slide 2: Discussion Points
Background
Current Leading Practice
Source elimination initiatives
Mafia Offer

## Slide 3: Background
Strategic Direction of the Noise Team
  Preventing Hearing loss instead of Preventing Compensating for hearing loss
  Emphasis is on Source Elimination
    4 T’s- Terminate, Treat, Transfer, Tolerate
  Current Reality - Noise has a lower priority compared to other Safety challenges (FOG, fatigue, T&M etc) and OH ( TB, HIV, Dust etc)

## Slide 4: Background
1st Leading Practice - Noise Elimination (2008)
  Electric Drilling Machine
    Potential to reduce noise by 200%
    Source Mine : AngloGold Ashanti – Tau Tona
    Demo Mine : Moab Khotsong
    Adopters : None other than the Demo Mine
    Not successful for various reasons
      Readiness for adoption:
        Required substantial R&D: only available for stope drilling
      Cost constraints:
        Required substantial refinement that proved to be expensive
        Only Leasing Option available
      Other:
        “Climate” – “Energy crisis” paved the way for selection as leading practice.

## Slide 5: Background
1st Leading Practice (cont.)
    Concept worth revisiting
      It is the ultimate Goal – part of zero harm
      Long term view
      Involving OEMs & Research institutions
    Current Noise at source - ± 108 dBA
      2013 Milestone : < 110 dBA & 2008 Milestone
      Legal Requirement : Noise Exposure: 85 dBLAeq,8h
      Shortfall: 25 dBA to be compensated for by HPDs

## Slide 6: Current LP – HPD TAS Tool
2nd Leading Practice - PPE and Administrative Control (2010 -2013)
  Hearing Protection Device, Training, Awareness and Selection Tool (HPD _ TAS)
    Enables Occupational Hygienists to select the correct HPD per occupation based on noise exposures and frequencies levels
    Training and awareness material – an explanation on the effects of noise, hearing protection devices and the usage, care and maintenance thereof
    10 Mining Houses (80 Shafts) are different stages of adopting
    Vergenoeg to consider adopting the LP
    Adoption process can be as short as 4 Months

## Slide 7: Source Elimination Activities
  Industry-wide strategy for a Buy and Maintain Quiet Initiative (BMQI)
  To provide the Mining Industry Leaders with a consolidated industry-wide strategy for a Buy and Maintain Quiet Initiative (BMQI) as well as a practical path-forward to execute the strategy
What is it?
    A standing decision from mining companies to procure equipment (machinery) and maintain existing equipment that comply with specific noise emission requirements
  Initiative has been endorsed by All stakeholders including the CEO s fatality elimination team
  Currently forming Working Groups to execute the strategy

## Slide 8: Source Elimination Activities
  Industry-wide strategy for a Buy and Maintain Quiet Initiative (BMQI) – cont.
Strategy manages noise at the ‘real source’
Utilises the collective demand from the industry will motivate OEMs to focus more on noise reduction as part of their product development
Cheaper to manage noise hazard at the design phase
  High hierarchy of controls will also impact on the Cost and Behavior

## Slide 9: Source Elimination Activities
  Source Elimination Repository
  Team compiles source elimination initiatives from the mining industry (Locally and international) for industry sharing and learning
  Repository is accessible on the MOSH website
    6 local initiates
    34 International initiatives (19 for Surface Mines and 15 for Underground Mines)
On-going exercise

## Slide 10: Future Leading Practice
  Custom Moulded HPD Management System
  Team completed a verification exercise and industry selected the Custom Moulded HPD Management System from Impala Platinum as a potential Leading Practice to be pursued by the Noise Team
  Impala Platinum is busy with the Refinements identified during the verification exercise

## Slide 11: Conclusion- Mafia offer from the noise Team
  Noise Team Invites Vergenoeng to participate in the Teams Activities
    Nominate an Industry Team Member
  ‘Low hanging fruits for Vergenoeng’
    Extensive assistance with the adoption of HPD TAS tool (4 Months exercise)
    Access to the source elimination repository
    Participation in the IBMQI

## Slide 12
Questions