## Slide 1: Vienna Dover
Fransa Owens

## Slide 2: Discussion points
Acts/DMR guidelines
COP stipulations
Vienna Dover
Application in the mining industry
Compliance requirements
  New recruits
  Periodicals
Rehabilitation programs
Risk management

## Slide 3: Acts/DMR guidelines
Health Professionals Council of South Africa (HPCSA) categorized the Vienna Dover as a psychometric instrument
  Specific stipulation to be used by Psychologist and other professionals for example Occupational and Speech therapist
Code of Practice (COP) on Railbound equipment : Section 8.5 makes provision for assessment of operators to ensure capability and competency
COP on the Minimum Standards of fitness to work
Mine Health and Safety Act – with reference to capability and competency requirements

## Slide 4: COP stipulations
The mandatory COP for RBE makes the following provisions in section:8.5. for the selection and placement of personnel to reduce the risk of incompetent persons operating and maintaining RBE. Listed in the assessment criteria are the following aspects:
Dimensions to be Tested | Training Centre | Occupational Health
Co-ordination | x | 
Ability to operate safely | x | 
Reaction time | x | 
Attention span | x | 
Vision test |  | x
Angle of vision |  | x
Night or colour blindness |  | x
Hearing and depth perception |  | x
Anthropometrics: Mass/Height |  | x

## Slide 5: Vienna Dover
Developed initially for the assessment of basic abilities of brain injured individuals
Expanded through research as a selection instrument across the world for
  Aviation
  Transport industry
  Mining
With the addition of rehabilitation programs linked to all assessment batteries increased the scope of application to rehabilitation and not only selection of candidates

## Slide 6: Vienna Dover: requirements of COP
Reaction Time
Signal detection
Two-hand coordination
Distance Estimation
Cognitron

## Slide 7: Application in the mining industry
In the mining industry the Vienna Dover has been used for the selection of operators since the 90’s
The main application has been the selection of new applicants or promotion as an operator
With new technology the scope of application has expanded to enable the assessment and rehabilitation of current operators
Currently the Vienna Dover is used by Gold Fields, Anglo Gold, Harmony and Platinum
Requirement to implement after a section 54 was issued in 2011 to Harmony on not applying the principles of the COP

## Slide 8: Compliance requirements
New Recruits | Periodicals
Assessment of all new applicants | Assessment with renewal of certificate of fitness
Promotions | Post injury / incident or accident
Transfers | Post illness

## Slide 9: Compliance requirements
The results would indicate the following:
  Recommended
  Recommended with reservations
  Not recommended
All the elements on the Vienna Dover can be rehabilitated unless there is loss of basic ability for example vision (not able to be corrected) ; permanent hearing loss and brain injury

## Slide 10: New recruits/promotions/transfers
Result | Recommendation
Recommended | Complete COF and proceed to training for capability and shaft for competency
Recommended with reservation | Occupation Health assessment to determine requirements linked to Minimum standards of fitness to work
 | Additional referral to training for rehabilitation program and job specific training
Not recommended | Not declared fit for occupation as operator
 | If a current employee allow for rehabilitation program on own time to enable to re-apply ( career development )

## Slide 11: Periodicals
Result | Recommendation
Recommended | Complete COF and proceed to training for capability and shaft for competency
Recommended with reservation | Occupation Health assessment to determine requirements linked to Minimum standards of fitness to work
 | Additional referral to rehabilitation program
Not recommended | Not declared fit for occupation as operator if there is medical grounds ( brain injury; loss of vision)
 | If a current employee allow for rehabilitation program and then re-assessment
 | Issue COF

## Slide 12: Periodicals – responsibility of Occupational health services
Assessment | Recommendation
Vision | To meet the requirements of the minimum standards of fitness to work
 | If vision must be corrected with spectacles then restriction to operate to be applied to license to stipulate that individual can only operate while wearing glasses
 | Issue COF
Peripheral vision | Signal detection fall-out area to determine the risk
 | Referral to rehabilitation
Hearing | If there is loss of hearing to correlate with outcome on Reaction time to indicate how this is influencing his response time assessment of the risk to determine fitness to operate
 | if hearing must be corrected with a hearing device , restriction to operate to be applied to the issuing of license

## Slide 13: Periodicals – responsibility of Occupational health services
Assessment | Recommendation
Two-hand coordination | Does not meet the requirements to refer to determine if there is a medical reason
 | Referral to rehabilitation to complete program
 | Issue COF
Distance estimation | Not meet or meet with reservations – determine if there is a medical reason for problem ( visual assessment )
 | Refer to rehabilitation
 | After rehabilitation completion determine fitness to operate – issue certificate to allow for process of training , capability and competency assessment
Cognitron | In the absence of cognitive impairment due to injury or illness
 | Refer to rehabilitation to complete program and allow for re-assessment
 | Issue COF

## Slide 14: Rehabilitation program
Health Services to provide in the form of cognitive rehabilitation programs
Programs available
  CogniPlus
  New programs designed continuously
Additional rehabilitation programs
  Visual perception
  Eye muscle movement ( Peripheral vision)
  Sequencing

## Slide 15: Risk management
Going forward the key element would be to manage the data on operators to determine
  Trends due to age of the operator
  Impact of exposure of the underground environment on basic abilities
  Accident analysis to determine abilities that could have had an impact to prevent similar incidents from occurring
  Refining of norms to determine criteria for selection and placement

## Slide 16: Questions