## Slide 1
by
L Kleynhans and L Smith
KOPANANG MINE
20 April 2015
Real-time Monitoring of Airborne Pollutant Engineering Controls

## Slide 2
Description of practice
Effectiveness of engineering controls
Schematic layout
The monitor
Project phases
The problem area
Results before and after
Pre- and post strategy
Benefits/Advantages
Key lessons learnt
Introduction of Dust Task Team
Vision
Contents

## Slide 3
  Following an identification process on the shaft, continuous monitors were placed on the intake air and direct return air side of an engineering control.
Baseline
  The ambient air condition is then monitored continuously in real-time and transmitted to a surface control room.
Monitor
  Should a “dust alarm” occur the control room operator will initiate a call out procedure to investigate the alarm.
Alarm
  Following investigation, an action log will be put in place to rectify the condition thereby preventing people to be over-exposed to harmful dust concentrations.
Action
Description of practice

## Slide 4
Engineering controls - effectiveness
Efficiency
The efficiency of engineering controls are normally dependant on the human factor
The strategy indicated a need to:
- test the effectiveness of the engineering controls
Other needs identified
A need was identified for continuous dust monitoring to get an overview on exposure of dust on employees working underground
- determine whether current engineering controls are
effective
14 Instruments were installed in a ventilation district underground
Installation of instruments

## Slide 5
Schematic layout (phase 1)
18 x/cut
9 x/cut
9 x/cut
44 Level
47 Level
50 Level
Stn Tips
Stn Tips
Stn Tips
Downcast
Shaft
Up-cast
Shaft
6A x/cut
Bank
KOP1 Ventilation District
Installations were done in the following areas:
  Surface, the downcast shaft
  Before and after various tipping areas
  Haulages and at the entrance to a development end.
This was done to measure the effectiveness of current engineering systems installed underground.

## Slide 6
The real-time monitor
Thermo MIE pDR-1000 DataRam

## Slide 7
Project phases
Phase 1
  Sensors installed in Kopanang Upper Mine
  Trends analysed from the real time sampling instruments proofed that engineering controls in that ventilation district is sufficient for the dust load
Phase 2
  Workers on 59 level complained about excessive dust during tipping operations
  With engineering controls installed, the dust problem persisted .
  Monitors were moved to 59 Level to assist with identifying the cause and source of the dust problems.
  Immediately after installation the trends indicated that although high dust readings were obtained during tipping, the main cause of dust was during the transfer between levels .
  It was decided that the transfer time should be moved to late afternoon, after the shift, thus reducing the employees exposure to dust
  All engineering controls were automated
  With the above process complete, the dust problem is effectively managed

## Slide 8
59-Level station diagram
Tips
Tips
Tips
59 Level

## Slide 9
Sensor results - Before

## Slide 10
Sensor results - After

## Slide 11
Pre-strategy

## Slide 12
Post-strategy

## Slide 13
Benefits/Advantages
Fast reaction time possible
Manage effectiveness of engineering control installed underground
Can monitor the whole mine simultaneously and continuously
You get the real picture of happenings underground in real time
No consumables and low maintenance
Move away from reactive management mode into a proactive approach
Real-time
Monitoring

## Slide 14
Lessons learnt
1
  Buy-in from multiple departments and stakeholders needed for this program to succeed. (Ventilation, Engineering, Mining etc)
2
  Proper training required ( Installation, operation and maintenance of instruments)
3
  Awareness campaign a necessity
4
  Spare instruments should be available
5
  The System will only work if it is properly and timeously maintained
6
  Establishing the Kopanang Dust task team, proved to be very beneficial to the success of this practise

## Slide 15
Success story
Dust Task Team
W Blaai
V Lengisi
E Semoeng
T Bulwa
V Msi
We are committed to make a D I F F E R E N C E

## Slide 16
Our vision
1
To monitor the whole mine simultaneously and continuously
2
Continuous improvement towards zero harm from silica dust and other airborne pollutants
3
Improved identification of problem areas – by getting the real picture in real time on activities as it is happening underground

## Slide 17
Closure
With Real-time Monitoring these days are gone FOREVER!!!
Thank You