## Slide 1: BEATRIX GOLD MINE WINCH DUST COVER PROJECT
Presented to MOSH Dust
19 March 2014

## Slide 2: Contents
Purpose and business need
Approach to the study
Exposured occupation
Initiative
Winch dust cover
Dust results
Project roll out
Lessons learnt

## Slide 3: Purpose and business need
The pupose of the this case study is to determine the feasibility to use the winch dust cover as an effective and efficient dust cover to reduce the exposure to silica dust in the mining environment.
In terms of the need of Sibanye Gold to eliminate silica dust exposure to its employees, Mining Unit 3 sourced and tested an effective and cost efficient winch dust cover to reduce the exposure of silica dust to winch driver employees.

## Slide 4: Exposed trends per Occupation (>0.05<0.1mg/m³)
Gravimetric sampling results indicated that winch drivers are most exposed
Intervention required to protect winch drivers
Chart: BEATRIX GOLD MINE TOP 20 OCCUPATIONS
| Winch Driver | Stope Rockdrill Operator | Mining Team | Senior G/T Leader | Stope Team | Loco Driver | Supervisor Operations | Gang/Team Leader | Engineering Utility Team | Night Shift Cleaner | Development Rockdrill Operator | Gang/Team Leader Transport | Boilermaker | Senior G/T Leader Mining | Conveyer Belt Attendant | Electrician | Fitter | Developer | Engineering G/T Leader | Stoper
N° | 61 | 47 | 39 | 29 | 29 | 22 | 19 | 18 | 15 | 13 | 12 | 12 | 10 | 10 | 9 | 9 | 9 | 8 | 8 | 8

## Slide 5: Approach to the study
The approach taken was to find a worst case scenario and explore ways in ensuring proper protection of winch drivers in their breathing zone whilst operating a winch without wasting any resources in getting the desired results.
An implementation plan starting at the training center and going down to the working faces.

## Slide 6: Initiative to reduce exposure
Investigations done to determine the reasons for driver exposure
Exposure as result of coiling of ropes around winch drum
  In the breathing zone of the winch driver
Clinton Randall initiated the idea of the winch drum cover
  Fits over the winch drum guard
Tests done show reduction in exposure levels
The Randall cover is now being introduced throughout Beatrix

## Slide 7: Winch cover

## Slide 8: Randall Winch Dust cover

## Slide 9: Randall winch dust cover

## Slide 10: Initial test done on the Randall winch dust cover
Chart: 
BEFORE | 0.5 | 0.603 | 0.536 | 0.44 | 0.563
Chart: 
AFTER | 0.38 | 0.331 | 0.298 | 0.333 | 0.294

## Slide 11: Comparative dust readings
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35
AFTER | 0.215 | 0.332 | 0.438 | 0.54 | 0.329 | 0.351 | 0.412 | 0.428 | 0.38 | 0.407 | 0.389 | 0.278 | 0.522 | 0.533 | 0.512 | 0.507 | 0.341 | 0.216 | 0.489 | 0.362 | 0.562 | 0.503 | 0.421 | 0.387 | 0.377 | 0.421 | 0.518 | 0.539 | 0.612 | 0.489 | 0.397 | 0.512 | 0.326 | 0.471 | 0.578
BEFORE | 0.317 | 0.425 | 0.576 | 0.572 | 0.517 | 0.525 | 0.612 | 0.785 | 0.549 | 0.554 | 0.471 | 0.486 | 0.783 | 0.811 | 0.726 | 0.685 | 0.495 | 0.386 | 0.617 | 0.487 | 0.788

## Slide 12: Comparative average dust readings (Before and After)
Chart: 
| DUST AVG. BEFORE | DUST AVG.AFTER.
WINCH COVER COMPARISON | 0.845 | 0.422

## Slide 13: Project roll out
Project roll out commenced at Beatrix West Section
  Section where project was initiated

## Slide 14: Lessons learnt
  Training of employees were a very important aspect of this project.
  Communication to employees.
  The project was not complicated and easy to implement.
  Winch drivers silica dust exposures at the winch areas were reduced by ±50%.

## Slide 15
Weekly communication 10 Mar to 16 Mar 2014
WINCHES AND RIGGING SAFETY
Always be aware of the hazards and risks associated with all tasks that you perform and take the required steps to safeguard yourself and others.
Light installed and working.
Signaling devices installed with bell wires the full length of the scraper path on both sides.
Winch barricaded installed and safe.
Lockout in place when winch is not in use to prevent unauthorized operation.
Holding down bolts secured and checked daily.
Make sure your winches are fitted with a dust cover for protection of the winch operator against dust and fine stuff from entering his eyes!!!!!
1
2
2
4
3
5

## Slide 16: Acknowledgement CLINTON RANDALL BEATRIX MANAGEMENT
???