## Slide 1: WINCH COVER PROJECT AT BEATRIX GOLD MINE
Presented at the
MOSH WORKSHOP
17 July 2013

## Slide 2: Exposure Trends
Gravimetric sampling results indicated that winch drivers are most exposed
Intervention required to protect winch drivers
Chart: BEATRIX GOLD MINE TOP 20 OCCUPATIONS
| Winch Driver | Stope Rockdrill Operator | Mining Team | Senior G/T Leader | Stope Team | Loco Driver | Supervisor Operations | Gang/Team Leader | Engineering Utility Team | Night Shift Cleaner | Development Rockdrill Operator | Gang/Team Leader Transport | Boilermaker | Senior G/T Leader Mining | Conveyer Belt Attendant | Electrician | Fitter | Developer | Engineering G/T Leader | Stoper
N° | 61 | 47 | 39 | 29 | 29 | 22 | 19 | 18 | 15 | 13 | 12 | 12 | 10 | 10 | 9 | 9 | 9 | 8 | 8 | 8
EXPOSURE TRENDS PER OCCUPATION (>0.05<0.1mg/m³)

## Slide 3: Initiatives to reduce exposure
Investigations done to determine the reasons for driver exposure
Exposure as result of coiling of ropes around winch drum
  In the breathing zone of the winch driver
Clinton Randall initiated the idea of the winch drum cover
  Fits over the winch drum guard
Tests done show reduction in exposure levels
The Randall cover is now being introduced throughout Beatrix

## Slide 4: Winch cover fitment
Winch Cover – Randall Cover

## Slide 5: Winch cover inspection flap

## Slide 6: Winch cover in use

## Slide 7: Results of initial tests
Winch cover initial tests done at start of project
Chart: 
BEFORE | 0.5 | 0.603 | 0.536 | 0.44 | 0.563
Chart: 
AFTER | 0.38 | 0.331 | 0.298 | 0.333 | 0.294

## Slide 8: Project roll out
Project roll out commenced at Beatrix West Section
  Section where project was initiated
113 Winches fitted with covers
Before and after readings:
  35 Before readings taken with an aerosol monitor
  21 After readings taken with aerosol monitor

## Slide 9: Comparative dust readings
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35
AFTER | 0.215 | 0.332 | 0.438 | 0.54 | 0.329 | 0.351 | 0.412 | 0.428 | 0.38 | 0.407 | 0.389 | 0.278 | 0.522 | 0.533 | 0.512 | 0.507 | 0.341 | 0.216 | 0.489 | 0.362 | 0.562 | 0.503 | 0.421 | 0.387 | 0.377 | 0.421 | 0.518 | 0.539 | 0.612 | 0.489 | 0.397 | 0.512 | 0.326 | 0.471 | 0.578
BEFORE | 0.317 | 0.425 | 0.576 | 0.572 | 0.517 | 0.525 | 0.612 | 0.785 | 0.549 | 0.554 | 0.471 | 0.486 | 0.783 | 0.811 | 0.726 | 0.685 | 0.495 | 0.386 | 0.617 | 0.487 | 0.788

## Slide 10: Average dust readings
Chart: 
| DUST AVG. BEFORE | DUST AVG.AFTER.
WINCH COVER COMPARISON | 0.845 | 0.422

## Slide 11: Acknowledgement
Barry Nel
Clinton Randall
Beatrix Management

## Slide 12: THANK YOU