## Slide 1
Winch Signalling System
F.B Mokgoja
Section Engineer
Moab Khotsong
13 May 2015

## Slide 2: Outline
Context and Purpose
Consultation Process
  Market Research
  Stakeholder Engagement
Design Parameters
  Functionalities of the system
  How it works
Technical Specifications
Installation Configuration
Challenges and Solutions
Way forward

## Slide 3: Context & Purpose
Technology project was initiated in line with AGA Strategic Pillars
  Removing people from risk
  Planning of work - BPF
  Behaviour – changing “Hearts and Minds”
Compliance to MH&SA - Chapter 8.4 - Scraper Winch and Mono-Rope installation
  8.4.1a
  8.4.2 a, b, c and d
Moab experienced increase in scraper accidents
(2009 – 2014)
  Avg
    6 All Injuries
    6 LTI
    3 SI
Improve the current systems to reduce accidents.

## Slide 4: Consultation Process
Market research was conducted with these considerations:
  Off the shelf- readily available
  Trial tested with performance results
  Reliable system
  Fit for purpose system – operating environment
  Competitive prices
  Compatible with the current electrical standards and MH&SA regulations
  The system must be plug and play and compatible with AGA winch starter box
Stakeholder Engagement
  Management and organized labour discussions
    Led to decision on the current system review
    Management of Change
  Design specifications and system functionalities were set
  Different OEM invited regarding the design and functionalities
    Reef Switchboard Manufacturers
    WPD Groups
    Bates Mining Suppliers
Improve the current system to reduce accidents.

## Slide 5: Design Parameters/Functionalities
Card reader facility – this prevents unauthorized operation of the winch.
Pre-start warning alarm – Audible through all the units and duration is 15 seconds, only then the driver can put the winch in motion.
Indication lights (LED) – Red/ green- this indicates whether it is safe or not to enter the scraper path
Lock out facility – on the tripped mode the driver will use his magnetic key to re-energize the system (where it tripped), only then can he put the winch in motion after pre -start warning alarm.
Emergency stop – this is achieved either by pulling the wire for longer periods or shining the cap lamp on the LED light of the unit continuously.
Signaling – for normal operation the pull wire must be pulled or cap lamp can be flashed on the unit for signaling purpose.

## Slide 6: Technical Specifications – winch signalling system
Winch Starter
  Plug and play facility
  Emergency push button
  LED display
  Earth path monitor
  Rectifiers – AC – DC
  Card reader
  Non-glaring winch light
Controller
  32V supply – light
  Built in adjustable timer
  LED lights
  Short circuit protection
Signaling unit
  24V supply
  Enclosed – moisture protection
  LED – Red/Green
  Light sensors
  Tripping features
  Magnetic key reset feature
Pull cable
  Length – 21m and 42m
  Plug and play connectors
Telephone
  Later addition
  Two way communication
Controller – with LED indicators
Winch starter
Signaling Device
LED lights
Plug and play connectors
Magnetic Key- resetting
Card Reader

## Slide 7: Installation configuration
winch starter
winch
signalling lights
signalling lights
Winch Signallaing Device
5m cable
42m cable
42m cable
42m cable
42m cable
42m cable
42m cable
21m cable
42m cable
winch controller
signalling lights
signalling lights
5m cable

## Slide 8: Challenges and Solutions -RSM
Magnetic key – failed to reset tripped unit
  OEM resolved the key
Cap lamp signaling failed
  Increased sensitivity
  Signal at an angle
  Activation distance at 4m
After sales –poor
  Technician on site for trial phase
  Engineers improved on R&D
High failure rate of signaling device
  Cable damages
  Installed short circuit protection device
Red Lights on Normal Mode
Green Lights on Tripped Mode
Driver explaining how it works

## Slide 9: Challenges and Solutions -WPD
Starter not compliant with AGA standard
No card reader facility
No lock out on the I LED
Positives
  Telephones
  High sensitivity on cap lamp signaling
  High illumination – I LED
Constraints
R&D costs
Timing
Future of the system
  Potential in the system
  Invest in R&D
Winch Controller
Starter Box with Plug & Play
I LED – Green Lights indicating it is safe to cross gully

## Slide 10: Way forward
Decided on Reef Switchboard system for roll-out.
  The system meet the requirements
  Work on R&D to sort future delays
  Make system more reliable
Purchased the system
  54 units
Identified critical areas for installation
Drawn up the installation schedule
  Allocate the resources and start the installations
  Train the artisans and winch operators on the new system
  Brief and communicate the employees
Monitor the system’s performance
  Impact on safety and production
  Impact on maintenance requirements
  Analyze and improve

## Slide 11: Questions & Discussions

## Slide 12: Thank You